## Slide 1
AutoCAM
Synthetic dataset generation for learned CNC toolpath planning
Inversion + shape prior · deterministic toolpaths · RL training
Design overview — feature & part taxonomies · two-phase pipeline

## Slide 2
The problem, and the approach
Learned CAM is blocked by data, not by models: there is essentially no public corpus of CNC geometry-to-toolpath examples. AutoCAM manufactures that corpus synthetically, then uses it to train a toolpath-generating model.
1
The data gap
No open dataset maps part geometry to valid machining toolpaths. This is the single bottleneck for an LLM/RL toolpath planner.
2
Generate by inversion
Toolpath→geometry is deterministic and cheap. We synthesise valid (geometry → toolpath → return) tuples instead of searching for them.
3
Two-phase system
Phase 1 builds the labelled dataset. Phase 2 trains an RL policy in a simulator that can exceed the dataset's own quality.

## Slide 3
Core principle: inversion with a shape prior
Because the shape is generated already machinable and the toolpath is produced by deterministic strategies, physical enforcement becomes proactive — engagement and MRR limits are respected up front, not repaired move-by-move.
Pure inversion
random moves → carve → whatever shape
Maximum diversity and minimum cost
But yields geometrically arbitrary blobs
An RL model trained on it generalises to blobs, not to real parts
Shape prior (chosen)
plausible shape → deterministic toolpath → carve
Machinability guaranteed by construction
Geometry stays part-like and sensible
Labels come from the confirmation carve, so they are process-true

## Slide 4
Classification of machinable features
Area / volumetric (2.5D)
Holes / axial
Standing / raised
Edge / detail
Contour / freeform
Machinable feature | Producing strategy | Governing constraint
Closed pocket | Adaptive / contour-parallel / zig-zag roughing | Internal corner radius ≥ tool radius
Facing / open pocket | Raster face passes to a plane | Stepover ≤ tool diameter
Slot / channel | Slot or trochoidal milling | Width ≥ tool Ø (else trochoidal)
Step / shoulder | Profile pass + Z-level roughing | Depth ≤ tool reach
Hole (through / blind) | Drilling or helical interpolation | Ø set by tool; helical for large Ø
Counterbore / countersink | Step-drill or helical, coaxial | Coaxial with the parent hole
Boss / island (+ ribs) | Contour milling around the standing feature | Wall / rib thickness ≥ minimum
Chamfer / edge break | Chamfer or lead tool along the edge | Angle set by tool geometry
Fillet / round | Ball / bull-nose tool along the edge | Internal fillet = tool radius (forced)
2D profile / contour | Profile pass with cutter compensation | Climb/conventional; radius comp
3D sculptured surface | Parallel / raster + waterline finishing | Monotone in Z; scallop set by stepover
Universal invariants (all features): monotone along the tool axis · internal radius ≥ tool radius · min channel width ≥ tool Ø · min wall thickness · depth ≤ reach · discretised Z levels.

## Slide 5
Classification of part categories
Each category fixes the feature mix, which in turn selects the generator (A height-field · B subtractive-by-construction · C parametric templates) and the realism source.
Plates & flanges
Dominant features Bolt circles, hole patterns, profiles, shallow pockets
Generator B + C templates
Realism Standard tables (DIN/ANSI) + LLM prior
Brackets & structural
Dominant features Steps, slots, ribs, mounting holes
Generator B
Realism LLM prior + templates
Enclosures & containers
Dominant features Deep pockets, thin walls, cavities
Generator B (wall-thickness critical)
Realism LLM prior; exercises multi-dexel
Manifolds & valve bodies
Dominant features Many holes, intersecting pockets, internal passages
Generator B — high complexity
Realism Templates; hardest, closed cavities
Freeform & sculptured
Dominant features Molds, dies, aero / ergonomic surfaces
Generator A + 3D finishing
Realism Parametric families; coverage via A
Housings & bosses
Dominant features Coaxial bores, faced tops, raised bosses
Generator B / C
Realism Templates + LLM prior

## Slide 6
How the taxonomies drive generation
The two classifications are the top of the funnel: they turn an abstract “make realistic parts” goal into a concrete, deterministic pipeline.
1
Part category
Plates, brackets, manifolds …
2
Feature mix
Which machinable features occur
3
Generator A/B/C
Height-field / subtractive / template
4
Deterministic strategy
Stepover & stepdown within limits
5
Toolpath + labels
gcode with process-true returns
MAP-Elites sits over the generator parameters to control dataset coverage; the morphological-opening validator gates every composition for machinability.

## Slide 7
Phase 1 — dataset generation
Almost entirely analytic and deterministic. The carver enters once, at the end, as a labeller.
DeepSeek-V4 meta-programmer
writes the generators, once
Shape generation · A / B / C
sampled in Python · MAP-Elites coverage
Morphological opening + validator
machinability gate · rest-material label
Deterministic toolpath → gcode
strategies within tool limits
Carver · confirmation carve
accepts gcode → process-true labels
Dataset
geometry → toolpath → return
EXISTING
1
LLM meta-programmer
Writes the generator programs once, composing vetted machinability-safe primitives — a realistic-part prior. Sampling stays deterministic in Python.
2
Shape generation A / B / C
Height-field, subtractive-by-construction and template generators, weighted; MAP-Elites enforces coverage of the behaviour space, not one optimum.
3
Opening + validator
Projects the target onto the machinable set, rounding internal corners to the tool radius; rejects sub-radius corners and thin walls. Residual = rest-material label.
4
Deterministic toolpath
Each operation expanded by a strategy with stepover/stepdown inside tool limits — valid by construction, no search. Emits gcode.
5
Carver · confirmation (existing)
The tested gcode-in carver runs once for process-true labels: scallop height, tool-radius fillets, rest material — what the process actually yields.
6
Dataset
Output tuples (geometry → toolpath → return), with validity and realism guaranteed by construction rather than filtered post-hoc.

## Slide 8
Phase 2 — RL training
The dataset only bootstraps; the carver then becomes the environment where the policy beats the imitation ceiling.
Dataset (from Phase 1)
geometry → toolpath → return
Bootstrap · offline RL
Decision Transformer on the dataset
Carver as RL environment
policy → gcode → reward · tri-dexel + engagement
Trained RL model
exceeds the imitation ceiling
EXISTING · EXTEND
↻ reward → policy
1
Dataset (from Phase 1)
The labelled (geometry, toolpath, return) corpus that bootstraps learning.
2
Bootstrap · offline RL
A return-conditioned sequence model (Decision Transformer) learns from the data; gcode is already a token sequence, mapping cleanly onto an LLM-style model.
3
Carver as RL environment (existing · extend)
RL paths are not valid by construction, so the carver validates them and computes true peak engagement / chip load. Needs the tri-dexel upgrade + a force layer — where the carver earns its place.
4
Trained RL model
Optimises reward directly in the simulator, so it can surpass the GA / imitation ceiling instead of merely copying dataset paths.

## Slide 9
The existing asset, and the build order
The tested gcode-in carver is used in two places with two maturities: ready today as the Phase-1 labeller, to be extended as the Phase-2 RL environment.
Ready today Phase-1 labeller
Feed the deterministic gcode; the carver returns the carved solid and the process-true labels (scallop, fillets, rest material). No new work beyond choosing what stays analytic.
To extend Phase-2 RL environment
Validate RL-generated paths and compute peak instantaneous engagement / chip load (not average MRR). Requires the tri-dexel upgrade for wall fidelity plus a force layer.
Recommended order
1
Define the contract
the common intermediate representation A/B/C emit and stage 3/4 consumes
2
Vertical slice on B
subtractive generator end-to-end → gcode → existing carver (closes Phase 1)
3
Add A and C
height-field and templates as extra shape sources against the proven interface
4
Open Phase 2 + tri-dexel
in parallel — tri-dexel and engagement serve only the RL environment

## Slide 10
Next step
Define the intermediate-representation contract
What a stage-1 generator emits, and what stage 3/4 expects to consume. It is the single interface that makes every downstream generator delegable and the whole pipeline buildable in parallel.